## Slide 1: Project Apollo
Why
  Ventilators need oxygen! (typical FiO2 0.3 … 1)
  Oxygen generation is a big problem in developing countries.
    No established infrastructure.
    Oxygen bottles are expensive
  People are already looking at alternative (local) ways for producing oxygen
What it is
  Goal of the Apollo prototype = enabling people around the world to build the prototype as fast as possible
  Focus = Simplicity and speed of build
    Open source, off-the-shelf materials
    Very low cost (aspirational target = $100 for 5 liters/min @ 90%)
  Final goal = Enable people to iterate and publish their own designs in the community
How to build it
  Follow the published build documentation
  Buy/source the materials (check out the BOM)
  Build the prototype
  Validate O2 concentration and flow. Use a good reference O2 and flow sensor for calibration
  Think about risk analysis and assessment: template for Apollo-derived design
  Document and iterate your own design. Publish your findings to the community!
Collaborations
  Peru, Afghanistan, Guatemala
Documentation
  http://project-apollo.org
  Already working on the next version
    Focused on safety, user experience and maintainability
    O2 compatible materials in the oxygen path
    Dedicated PCB controller board, sensor integration, valve operational sensing
      3” TFT touch screen for diagnostic messages, medical-grade buzzer
      Auto-tuning (valve timing, auto-adjusts to changes in compressed air input pressure)